## Slide 1: NDNoT: NDN-IoT Framework – Example Application “Flow”
Zhehao Wang
June 15, 2016
Notes: Flow with a different name

## Slide 2: Introduction
Notes: Continue fleshing this out
Consider moving into tech report / documentation if that fits better

## Slide 3: IP-IoT challenges
Complex Solutions to Simple Communication Needs
Limitations of Channel- and Session-based Security
Poor Integration of Local Communication

## Slide 4: NDN basics
Basic Protocol: Named Data Retrieval
Data-centric Security
Name-based Forwarding
In-network Storage

## Slide 5: NDNoT: functionalities
NDNoT (Named data network of things) is an IoT framework running on top on NDN, featuring following functionalities:
  Naming things, devices, and their data
  Device bootstrapping [1] and service/capability discovery [2]
  Schematized trust [3]
  App-level pub/sub [4]
  Global internet integration
Notes:   Other bullets listed include:
  (Name based access control, not reflected by Flow)
  (Data aggregation, not reflected by Flow)
  (Efficient multi-party communication, reflected by Flow discovery?)
App-level pub/sub (reflected by the seq-based data fetching, maintenance of outstanding interest of Flow)
  Global internet integration (prefix proposal, to be nailed down)

## Slide 6: NDNoT: deployment scenario
  Source: Wentao Shang, NDN Smart Home Design, 2014
Notes: Haitao: revise before “naming” section; send Haitao pointer for implementation
Summary and documentation of omh repositories
Huawei’s expectations of Flow

## Slide 7: Flow: user experience
User buys the game “Flow” (hardware + software), and installs in his home environment with minimal configurations
Multiple users interact with the following components of the game
  A person tracking system which tracks and publishes multiple persons’ physical locations in the space
  Arduinos (RFduino) connected to a bluetooth central and carried by users. Each publishes data from its gyroscope shield
  Phones connected to local wifi and carried by users. Each checks the status of the environment, and sending out commands that thematically influence the environment
User authorizes each device in the game environment; unregistered devices’ data will not be trusted by the game
Each device/component discovers other “registered” devices, and could choose which one to interact with
Notes: More user centric description (need info from Eitan)
Look at Huawei proposal, match the terminology
NEST

## Slide 8: Flow: components
Component | Device | Role
OpenPTrack (opt) | Linux workstation machine | Produces time-series data (location of multiple tracked persons) at 30Hz
Mobile website | Mobile phone | Produces environment control commands and consumes environment status
Virtual camera control | RFduino | Produces NDN data from its gyroscope shield, packetize, and send to bluetooth central (RPi) via bluetooth
Controller | RaspberryPi2 | Serve as the trust anchor, and runs as NDN-pi[1] controller
Unity3D game engine | OSX machine | Consumes opt, phones, and Arduino data; and does visualization
Each component also runs discovery, and schematized trust
There may be multiple instances of each component in the system
Notes: Mention multiple home gateways explicitly for NDNoT,
draw home network cloud; wentao slides

## Slide 9: Naming
Notes: Continue fleshing this out
Consider moving into tech report / documentation if that fits better

## Slide 10: NDNoT: name prefix assumption
NDNoT system runs in a space which can be represented by a (hierarchical) name
  This name could be a globally unique network-related ID, e.g. “/ucla/melnitz-hall/room-1469”, or a local one for local environment e.g. “/my-home/living-room” (for bridging with global Internet, forwarding hints and encapsulation could help, but requires detailed proposal depending on what we want to achieve)
  This name is used as the prefix for the IoT system (“root prefix” as in NDNoT paper). It could be configured by the owner of the space, or automatically configured by running autoconfig

## Slide 11: Flow: namespace as in NDNoT framework
Notes: Show it before introducing names
Use globally unique prefix (distinguish yourself from others), other people visiting your home; getting the globally unique ID for home
Why manufacturer namespace with manufacturer prefix? the two purposes
Slides: goal of these namespaces first;
Profile, being in a type namespace (capability); or device namespace
User namespace, separate (people); consumption namespace
“Configured thing” namespace, device namespace (as in my home), and debatable manu namespace

## Slide 12: NDNoT: namespaces
Each device in the game can be named from three levels
  Application/thing level: name the thing
    An application-specific “label” given by the user
    Used for the exchange of application data
  Device level: name the device in a space
    Associated with some physical property of the device to identify the device in a space
    Used for device control and status feedback
  Manufacturer level: name given by the manufacturer
    The name of device given by the manufacturer when produced
    Used for initial device verification, and manufacturer-based querying
Notes: Instantiation of the framework, but still framework level, not necessarily paper idea

## Slide 13: Flow: namespace example
As an example of the different namespaces, for a Samsung phone in the game “flow-123” labeled “phone-A”, its names on different levels could be
Notes: Story of where the names prefix come from; scenario of moving to home, and giving names to rooms

## Slide 14: NDNoT: device-level naming
Devices-level: (blue: configured by user)
  Prefix: root prefix in slide #7
  Device-id: some physical property of the device
  Data-instance, (defined by manufacturer?) e.g
    “_meta/capabilities”, what this device can publish
    “cmd/add”, the command that attempts to add this device (to e.g. a game system);

## Slide 15: NDNoT: thing-level naming
Thing-level:
  Prefix: root prefix in slide #7
  Thing identifier could be several application specific name components (or labels)
  Data instance, defined by application developer, e.g.
    “lights/on/”, a specific command that turns lights on
    “pH/201412021339”, a soil pH measurement value at a specific time point

## Slide 16: Flow: thing-level naming, opt
In Flow, a thing-level name is a name in the application, and for the components that produce data, we have
OpenPTrack (namespace design)
  Tracks: /my-home/living-room/flow1/opt1/<start_ts>/tracks/<track-id>/#seq
  Hints: /my-home/living-room/flow1/opt1/<start_ts>/track_hint/<ts>
  (* Where flow1 is the game identifier, and opt1 is the application label of the component)
Notes: Where “flow1” goes

## Slide 17: Flow: thing-level naming, mobile/Arduino
Mobile / Arduino
  Mobile data: /my-home/living-room/flow1/Arduino1/gyroscope/#seq
  Metadata: /my-home/living-room/flow1/phoneA/_meta/
    Branch “_device”: contains a pointer back to the name of the device producing it;
    Branch “_status”: contains the application level info such as “producing rate”, “latest sequence number”, etc

## Slide 18: Trust
Notes: Continue fleshing this out
Consider moving into tech report / documentation if that fits better

## Slide 19: NDNoT: threat model
Unauthorized device masquerading as trusted device
Notes: Subsection slides;
add access control design
NIST workshop Halderman talk
Start with first principles and security properties: only authorized and authenticated devices can publish to make it easier to follow (positive statement)

## Slide 20: NDNoT: trust
NDNoT uses schematized trust [3], where trust decisions leverage the structure of names to schematize decision-making on a packet-by-packet basis
Schematized trust uses a schema file to define expected relationship between a data name and a keyLocator, and forms a hierarchical structure
In an IoT context, some gateways or controllers could be introduced as trust anchors
Notes: Give example of the last bullet, what the root of trsuts are for different namespaces
Start with authenticating each device, then talk about the trust relationship (maybe not the name details, otherwise bootstrapping could come first)
Specify the assumptions (what you can get out of manufacturers, eg); split authentication (manufacturer) and authorization (integration into the system)
Sketch out the ideas, not introducing the mechanisms here; trust schema being implementation

## Slide 21: Flow: application trust schema
Flow trust schema defines the following relationship:
Notes: JB: How is app itself sign? Does app configure device directly
Not sure if I understand the question
Flow app code trust;
illustrate trust for three namespaces

## Slide 22: Flow: manufacturer and code/binary trust schema
Trust schema in manufacturer namespace
Trust schema in application binary data namespace (add this to flow namespace as well?)

## Slide 23: Flow: trust schema dissemination
Flow trust schema is cross-namespace
  The device “Arduino/serial-5678” is allowed to produce under “Arduino1/gyroscope” for game “flow1”, but not “phoneA/thematic” data
This cross-namespace binding is conveyed in the bootstrapping process and registered at the controller. Interested consumers fetch and verify the updated trust schema from controller (e.g. via ts/#seq based outstanding interest)
Notes: *Question: is the assumption “if a user decides to trust a device, then he trusts the device to produce any data” reasonable for this application?
This would be a simplification for trust design as it makes it static.
Though the answer’s likely no, and the complexity of building, and more importantly disseminating the (updated) trust schema, likely depends on how far the assumption goes: “I trust any wii-controllers to provide button press data”, or “I only trust wii-controller 1234 to provide button press data for device labeled ‘B’”. At this point, what’s the most reasonable assumption to make?
Device authentication when installed, this info used later on.
Every time do application authorization of publishing?
You don’t add device to your app
Device installation authentication
Gateway authorization: gateway discovers tells device what they should publish under

## Slide 24: NDNoT: bootstrapping trust
Follows the bootstrap process introduced in NDN-pi [1]
Bootstrap trust between a controller and a device via a shared secret established offline (e.g. NFC scan, manual input PIN)

## Slide 25: Flow: bootstrapping trust
In Flow, the bootstrapping process looks like

## Slide 26: Discovery
Notes: Continue fleshing this out
Consider moving into tech report / documentation if that fits better

## Slide 27: NDNoT: discovery
NDNoT suggests service and capability discovery via the help of controllers: devices register capabilities with controller during or after the bootstrap process

## Slide 28: Flow: discovery
Flows runs distributed (Sync-based) discovery (NdnCon discovery) [2]
  Multicast namespace:
  /my-home/living-room/devices/discovery/<digest>
  Digest is a hash of names of devices currently known by the data’s producer; Data content is the list of names known by the data’s producer
  Each device, upon being certified, will add its own device name to this list and reply to interests for the old digest
  Each device, upon receiving data, will issue device metadata interest using names in the list to know if the device’s in, and what data-type it’s publishing
Notes: Expand the discussion; add sequence; progression of exchanges of messages; specific names
Basic building blocks for achieving authenticable, in trust; HMAC signature?
What this thing does; what assumptions should come first
Idea’s that Arduino’s no different from other devices from design in terms of security; Arduino could have its key pair; Arduino to RPi has to be verifiable, Rpi could sign the data coming out from it, sounds like a similar process with the trust schema dissemination slide
NIST may have different plans

## Slide 29: Flow: discovery sequence
For example, device 2 discovers device 1 (device 1 goes through the same sequence to discover device 2)

## Slide 30: Constrained Devices
Notes: Continue fleshing this out
Consider moving into tech report / documentation if that fits better

## Slide 31: NDNoT: constrained devices
Long, human readable NDN names may not be desirable: name encoding techniques
Generation, assignment and evaluation of keys can be done on more powerful devices; and such keys can be stored on constrained devices
Achieving access with the help of an authorization server (NDN-ACE)
Push-style communications (encode data in interest, or long-live and refreshing PIT entries)
Notes: Which ones we use

## Slide 32: Flow: constrained devices
Initial implementation of Flow uses RFduino, who
  Acts as a bluetooth peripheral, does not run forwarder, but runs ndn-cpp-lite library to
    receive and decode interests
    packetize NDN data
    generate HMAC for data it produces
    send data to the central via bluetooth
  Trusts a “base station” (could be the controller, or someone trusted by the controller in Flow) from offline means (e.g. manual PIN input as in NDN-pi) and has a shared secret which no one else (including the bt central if it’s not the base station) knows
Notes: JB: All data packets must be verifiable. So Arduinos would use HMAC style signatures (if needed) that a base station (but not everyone) could authenticated because of a shared symmetric key.

## Slide 33: Flow: constrained device authorization
Idea: authorizing a constrained device, and later verifying the data it produces should be similar with authorizing / verifying other devices; To add an RFduino to the home environment:

## Slide 34: Flow: constrained device data verification
Base station stores a mapping between RFduino’s bluetooth name and NDN name, and associate the RFduino’s key pair with that NDN name. For an RFduino to be added, base station needs to process the controller’s “add device” command for the device so that device’s cert is signed
RFduino produces data name, content and HMAC using the symmetric key it shared with the base station, and sends the message to base station. Base station verifies, finds the corresponding key pair, generates a signature, and packetizes as NDN data packet
Consumer verification of data from constrained device is the same as the verification of data from elsewhere

## Slide 35: Summary
Notes: Continue fleshing this out
Consider moving into tech report / documentation if that fits better

## Slide 36: References
[1] A. Bannis, J. Burke. Creating A Secure, Integrated Home Network of Things with Named Data Networking, Tech. Rep. NDN-0035, NDN, 2015
[2] Z. Zhu and A. Afanasyev. Let's ChronoSync: Decentralized dataset state synchronization in NDN. In ICNP, 2013.
[3] Y. Yu, A. Afanasyev, D. Clark, K. Claffy, V. Jacobson, and L. Zhang. Schematizing Trust in Named Data Networking. In ICN’15, 2015
[4] (In progress) W. Shang, M. Zhang, A. Afanasyev, J. Burke, L. Wang, L. Zhang. Publish-Subscribe Communication in Building Management Systems over Named Data Networking. In ICN’16, 2016

## Slide 37: Thanks
Notes: Continue fleshing this out
Consider moving into tech report / documentation if that fits better

## Slide 38: Appendix: scenarios in Flow installation and usage

## Slide 39: Scenario: initial naming of a home
User has several routers in his home; each one may be covering several rooms
When installing the routers at home for the first time, user will be asked to provide the names each router should use, the prefixes they should serve
  For example, router serial-1234 should generate key pairs for identity “/alice-home/router1/”, and should serve “/alice-home/living-room” and “/alice-home/study”)
The user could set up one master router (gateway) for the home, and add other routers from the gateway
For a flow game running in the living room, user could choose to have the corresponding router sign the certificate of the game’s controller
Notes: This identity “/alice-home/router1” is still considered to be in device namespace

## Slide 40: Scenario: buying the game and installing at home
The game would come with a controller (not necessarily a router, maybe an RPi 2 that serves as the default trust anchor when you buy the game), a machine running opt, and a set of IoT devices (RFduinos), each with corresponding Flow component code installed, and has a preconfigured prefix, for example “/ndn/local/flow”, and with trust relationship already established: anchor cert is installed in each device and all device certs are signed.
The user would use some UI to set the controller’s prefix and his game instance name
Controller would inform its discovered devices that there’s an “installation”, so devices would use the new name to create key pair, and ask the controller to sign their new certs (during initial inform, the controller could include a challenge and expect response in devices’ new sign requests, so that no attackers could masquerade during the installation process)
Notes: Huawei is providing the ISP-level service that enables these networks to be linked

## Slide 41: Scenario: adding a newly bought device (Phone with NFC)
A new Samsung phone would come with a certificate signed by Samsung. Verify it with Samsung. Then install Flow phone app (or run web browser), set the installation prefix to the prefix controller’s using, configure the application id (label), and connect to local network (register right prefixes). Phone generates its key pair in device namespace and self-sign.
Controller has an NFC tag reader, to add the new phone, scan its NFC tag using the controller
Controller would find out the device GUID and create a shared secret based on the NFC tag, and initiate “add device” by sending out interest to the phone
Phone would reply with the application label it uses and what types of data it produces, and user confirms on controller to proceed with phone cert retrieval and signing, meanwhile controller updates the trust schema and informs all discovered consumers of this update (or they always keep outstanding interest for next schema)

## Slide 42: Scenario: replacing a device using the same application level name
Imagine that the old “wii-controller-A” breaks, we replace it with a new one also called “wii-controller-A”
Just follow the steps in the add device scenario in the previous slide